| SUBJECT/TITLE: | Airborne Particles/Contaminant Control |
| --- | --- |
| PURPOSE: | Containment of dust during maintenance operations in inpatient areas. |

A. During the performance of maintenance in inpatient areas that could involve the release of dust or other contaminants in the area, a double barrier or environmental containment unit with a hepa filter shall be used.

1.	The patient shall be removed from the area.

2.	Negative pressure shall be maintained during work and clean up.

3.  The Engineering Services staff shall ensure that the barriers being used are 	properly sealed.

4.	For large maintenance or construction projects, an ANTEROOM envelope shall 	be constructed prior to the start of the project.

5.	The dust barrier or environmental containment unit will be wiped down prior to 	removal.

6.	Environmental Services – Housekeeping will be notified when the project is 	complete so the area can be re-cleaned.

RELATED AND SUPPORTING DOCUMENTATION:

•	Capital Management

700, Project Risk Assessment

Source: UI Healthcare Engineering Services

Date effective: May 27, 2001

Date Reviewed: July 22, 2016