| SUBJECT/TITLE: | Failure of Nuclear Medicine Air Handling Units #3 and #6 and or Exhaust Fans |
| --- | --- |
| PURPOSE: | To maintain operation of Air Handlers unit #3 and #6. |

A. PROCEDURE:

1.	Notify the staff in the Nuclear Medicine area at 356-1911 about the failure 		and the areas affected.

2.	Check the affected Air Handling Unit for the following:

A. Control Failure

1) Check the pneumatic - electric switch.

2) Check the operation of the unit on the Siemens 							Computer System.

B. Electrical Problems

1) Check disconnect for power.

C. Mechanical Failure

1) Check the belts, bearings and motors.

3.	If the Environmental Systems Mechanic is unable to identify the problem, 			contact the lead person, Operations Manager of Engineering Services and 		the Director of Engineering Services, as required.

4.	Notify the staff in Nuclear Medicine at 356-1911 as to the status of the Air 		Handling Unit and the length of time required to effect repairs for their 			planning purposes.

Related and Supporting Documentation

•	Utilities Management Program, Engineering Services Policy C-001

•	Safety Reference Cards

•	On Call and Call Back Procedures, Engineering Services Policy A-115

Source: UI Healthcare Engineering Services

Date effective: July 1, 1995

Date Revised: Aug.13, 2001

Date Reviewed: April 19, 2016