| SUBJECT/TITLE: | Operating a Gas Powered Hedge Trimmer |
| --- | --- |
| PURPOSE: | Safe operation of a gas powered hedge trimmer. |

I. The Engineering Services Department will provide proper training to staff operating gas powered hedge trimmers.

II. Modification to Daily Attire Requirements: Long Pants or equivalent such as chaps- shall be worn. No exceptions will be allowed unless approved by the Director.

III. Required PPE:

- Dust Mask as needed			5. Safety Shoes/ Boots with Reinforced Toe

- Safety Googles or Face Shield		6. Leather Chaps or Equivalent

- Hearing Protection, Ear Plugs, or Muffs	7. Appropriate Clothing: Long Sleeves, Long 							    Pants

- Leather or Other Appropriate Gloves		8. Hard hat as needed

IV> Required Training:

- Read, understand, and follow manufacturer’s safety instructions

- Training with qualified person prior to use

| TASK | HAZARDS | CONTROLS |
| --- | --- | --- |
| Preparing Saw | Hand Injuries | Wear leather (or other durable) gloves, use caution when handling blades |
| Fueling/Oiling | Fire | Always add fuel outdoors, ensure fuel cap is secure before use |
|  |  | Do not add fuel if near open flame or sparks |
|  |  | Clean-up fuel spills immediately; do not start engine until fumes have dispersed |
|  | Chemical Exposure: Skin or Eyes | Wear appropriate gloves and eye protection when fueling |
| General Use | Bodily Injury | Wear appropriate clothing, including boots, long pants, and chaps as needed |
|  |  | Keep all guards and shields in place |
|  |  | keep hands, clothing, and hair clear of all moving parts |
|  |  | If working overhead or under other workers, wear hard hat |
|  | Inhalation of Dusts or Particles from Cutting | Wear dust mask as needed |
|  | Eye Injury | Wear safety goggles or face shield to prevent eye/face injury from flying wood chips or vegetation, etc |
|  | Hearing Damage | Wear hearing protection: ear plugs or earmuffs |
|  | Foot Injury | Wear safety shoes or boots |
|  | Injury to Others | Use cones, barricades or other department staff members to keep others clear of area. Staff members may need to wear PPE. |
| General Use | Bodily Injury from Vehicles, Bicyclists, etc. | Place signs, cones, barricades, caution tape and lookouts as needed |
|  |  | Wear reflective safety vests |
| Additional Precautions for Fuel Powered Engines | Injury and Fire | Always operate in well-ventilated area |
|  |  | Never fuel engine while running |
|  |  | Stop engine before performing maintenance or trouble shooting |
| Procedure for Malfunctioning or Broken Equipment | Bodily Injury | Obtain tag from shop, mark equipment "Do Not Use"- Specify problem |
|  |  | Notify shop and/or take equipment to shop |

Training: Operation Of Gas Powered Hedge Trimmer

Training Video: https://www.youtube.com/watch?v=gHJCDJsAx2k

DO NOT use this machine unless you have been trained in its safe use and operation. Training must be documented and signed by the employee before use.

| Description of Work: | Operating A Gas Powered Hedge Trimmer |
| --- | --- |
|  | Potential Hazards: Exposed moving parts with the potential to cause harm through entanglement, impact and cutting, shearing or crushing injuries, ergonomics, vibration, noise, slips, trips and falls and dust. |
| Personal Protective Equipment (PPE) Required |
| Gloves | Face Masks | Eye Protection | Welding Mask | Appropriate Footwear | Hearing Protection | Protective Clothing |
| Safe Work Procedure Checklist: |
| 1. PRE-Operation: Check for obvious faults and defects including fuel leaks or damage. Identify ON/OFF switch. Wear adequate and appropriate PPE. 2. Operation: Exercise caution in relation to exhaust heat. Hold trimmer firmly with both hands. Ensure firm footing. Move your body with the trimmer; do not twist from the waist. Do not cut over shoulder height. Do not walk with trimmer while cutter is in motion. Do not use in the rain or wet conditions. 3. POST-Operation: Ensure cutters have stopped before removing waste material Ensure cutters have stopped before placing trimmer on the ground. Ensure equipment is returned to storage area after use. |
| Competent Persons (The following persons are authorised to operate equipment. |
| Date: | Name: | Trainer Signature: |

Source: UI Healthcare Engineering Services

Date effective: July 1, 2016

Date Reviewed: July 1, 2016