| SUBJECT/TITLE: | Operating a Skid Loader |
| --- | --- |
| PURPOSE: | To facilitate proper operation of a skid loader. |

Policy Statement:

The Engineering Services Department will provide proper training to staff that operate any skid loader / skid steer loader.

Required PPE:

- Leather or Other Appropriate Gloves                 5. Safety Shoes/ Boots with Reinforced Toe
as needed					5. High Visibility Vest

- Hard Hat as needed

- Safety Glasses as needed

Required Training:

- Read, understand, and follow manufacturer’s safety instructions

- Training with qualified person prior to use

| TASK | HAZARDS | CONTROLS |
| --- | --- | --- |
| Preparing Job Site And Equipment | Trips | Clear area within work zone; Remove trip hazards and/ or mark clearly hazards with cones, etc. |
|  | Cuts | Wear gloves when checking tires and attaching implements |
|  | Exposure to Oil/Coolant | wear safety glasses and gloves if adding fluids |
|  | Bodily Injury to Others | Identify work zone with cones, barricades and other means necessary to keep pedestrian and other traffic out of the work zone |
| Operational Considerations | Bodily Injury | Wear reflective safety vest and hard hat. (Safety glasses as needed) |
|  |  | A pre-job discussion should occur to ensure both the equipment operator and assisting workers understand the scope of the project |
|  |  | Operator should keep watch for ground workers near equipment and ensure they are aware of operator's intended direction of movement. Use spotter as need to warn/watch for ground workers. |
|  |  | Ground workers should watch operator and equipment, staying clear of equipment's path |
|  |  | All works need to be aware of changing conditions at work site area. |
| Equipment Operations | Falling Off Equipment | Fasten seatbelt or use safety bar properly |
| Equipment Operations | Rollover | Do not overload bucket |
|  |  | Do not use Skid Steer on uneven ground |
|  |  | Operate within manufacturer listed stability speeds |
|  |  | Keep load balanced |
|  | Bodily Injury to Operator | Never reach into areas with moving parts such as tires, hydraulics arms, and bucket. |
|  |  | Never leave equipment running to clear tires or troubleshoot problems |
|  |  | Do not operate damaged or malfunctioning equipment. |
|  |  | Be aware of changing conditions at worksite |
|  |  | Wear hard hat if at risk from being struck from falling materials or other objects in or outside of unit |
| After operations or during periods when area is not occupied by workers | Bodily Injury to Workers and Others | Operator should always leave equipment with bucket/attachments down. |
|  |  | Operator should ensure equipment is secured/locked out so cannot be used by unauthorized personnel. |
|  |  | Workers should secure job site with barricades, cones and signs to warn others to keep out of work site area. |
|  |  | Supervisor may place employee to watch job site if extreme hazards exist. |
| Servicing or Repair of Equipment | Bodily Injury | Obtain tag from shop, mark equipment "Do Not Use"- Specify problem |
|  |  | Notify shop and/or take equipment to shop |

Training: Operating A Skid Loader / Skid Steer

Training Video:

https://www.youtube.com/watch?v=2Is6c1Znu1E&list=PLD26EEC73C0577516&index=1

DO NOT use this machine unless you have been trained in its safe use and operation. Training must be documented and signed by the employee before use.

| Description of Work: | Operating A Skid Loader / Skid Steer |
| --- | --- |
|  | Potential Hazards: Exposed moving parts with the potential to cause harm through pinching, impact and crushing, shearing injuries, ergonomics, vibration, noise, slips, trips and falls and dust. |
| Personal Protective Equipment (PPE) Required |
| Gloves | Face Masks | Eye Protection | Welding Mask | Appropriate Footwear | Hearing Protection | Protective Clothing |
| Safe Work Procedure Checklist: |
| 1. PRE-Operation: Check for obvious faults and defects including fuel leaks or damage. Identify ON/OFF key switch. Wear adequate and appropriate PPE. 2. Operation: Use of seat bar or seat belt. Keep hands and feet inside unit. Use both hands on steering controls. Ensure firm footing. Always keep eyes on direction of travel. Do not have riders. Do not allow people to approach when arms are in raised position while in use. Know the acceptable amount of load each attachment can safely handle. Keep bucket or attachment as low as possible; always load/unload on flat terrain. Use smooth operation on controls. 3. POST-Operation: Ensure no damage has been made to unit or fluid leaks Ensure unit is parked on flat terrain and parking brake set. Ensure equipment is returned clean to storage area after use. |
| Competent Persons (The following persons are authorised to operate equipment.) |
| Date: | Name: | Trainer Signature: |

Source: UI Healthcare Engineering Services

Date effective: Jan 11, 2016

Date Reviewed: June 30, 2016