| SUBJECT/TITLE: | Operating a Kubota Riding Mower |
| --- | --- |
| PURPOSE: | Safe Operation of Kubota Riding Mower. |

Policy Statement:

The Engineering Services Department will provide proper training to staff that operate any Kubota Riding Mower.

Required PPE:

- Safety Glasses				4.   Safety Shoes/ Boots with Reinforced Toe

- Dust Mask as needed			5.   Hearing Protection, Ear Plugs, or Muffs

- High Visibility Vest as needed

Required Training:

- Read, understand, and follow manufacturer’s safety instructions

- Training with qualified person prior to use

| TASK | HAZARDS | CONTROLS |
| --- | --- | --- |
| Preparing Job Site And Equipment | Trips | Clear area within work zone; Remove trip hazards and/ or mark clearly hazards with cones, remove large branches, etc. |
|  | Cuts | Wear gloves when checking tires and attaching implements. |
|  | Exposure to Oil/Coolant | Wear safety glasses and gloves if adding any fluids. |
|  | Bodily Injury to Others | Identify work zone if needed use cones, barricades and other means necessary to keep pedestrian and other traffic out of the work zone. |
| Operational Considerations | Bodily Injury | Wear reflective safety vest when traveling on roadways. |
|  |  | A pre-job discussion should occur to ensure both the equipment operator and assisting workers understand the scope of the project when needed. |
|  |  | Operator should keep watch for ground workers near equipment and ensure they are aware of operator's intended direction of movement. Use spotter as need to warn/watch for ground workers. |
|  |  | Ground workers should watch operator and equipment, staying clear of equipment's path and mower discharge. |
|  |  | All workers need to be aware of changing conditions at work site area. |
| Equipment Operations | Falling Off Equipment | Ensure firm footing and use of handle grips as needed |
| Equipment Operations | Rollover | Do not turn sharply on hill sides at high speeds |
|  |  | Do not load/unload riding tractor on uneven ground |
|  |  | Operate within manufacturer listed stability speeds |
|  | Bodily Injury to Operator | Never reach into areas with moving parts such as tires, mower deck belts, PTO attachments. |
|  |  | Never leave equipment running to clear tires, debris from belts or troubleshoot problems |
|  |  | Do not operate damaged or malfunctioning equipment. |
|  |  | Be aware of changing conditions at worksite. |
|  |  | Be aware of fluid leaks. |
| After operations or during periods when area is not occupied by workers | Bodily Injury to Workers and Others | Operator should always leave equipment with PTO disengaged and turned off. |
|  |  | Operator should ensure equipment is secured/locked out so cannot be used by unauthorized personnel. |
|  |  | Workers should secure job site if needed with barricades, cones and signs to warn others to keep out of work site area. |
|  |  | Supervisor may place employee to watch job site if extreme hazards exist. |
| Servicing or Repair of Equipment | Bodily Injury | Obtain tag from shop, mark equipment "Do Not Use"- Specify problem |
|  |  | Notify shop and/or take equipment to shop |

Training: Operating a Kubota Riding Mower

Training Video: https://www.youtube.com/watch?v=zgDadsKffRw

DO NOT use this machine unless you have been trained in its safe use and operation. Training must be documented and signed by the employee before use.

| Description of Work: | Operating A Kubota Riding Mower |
| --- | --- |
|  | Potential Hazards: Exposed moving parts with the potential to cause harm through pinching, impact and crushing, ergonomics, vibration, noise, slips, trips and falls and dust. |
| Personal Protective Equipment (PPE) Required |
| Gloves | Face Masks | Eye Protection | Welding Mask | Appropriate Footwear | Hearing Protection | Protective Clothing |
| Safe Work Procedure Checklist: |
| 1. PRE-Operation: Check for obvious faults and defects including fuel leaks or damage. Identify ON/OFF key switch. Wear adequate and appropriate PPE. 2. Operation: Always be looking ahead for obstacles. Watch for trees, buildings, overhangs and other obstructions. Allow enough room to safely pass between obstructions. Be careful not to get too close. Check overhead clearance before passing beneath branches, awnings and other obstructions. Keep hands and feet on unit. Ensure firm footing. Always keep eyes on direction of travel. Do not have riders. Do not allow people to approach when PTO is engaged. Know the limits of the machine. Use smooth operation on controls. Engage PTO at low throttle. 3. POST-Operation: Ensure no damage has been made to unit or fluid leaks. Ensure unit is parked on flat terrain and parking brake set. Ensure equipment is returned clean to storage area after use. |
| Competent Persons (The following persons are authorised to operate equipment.) |
| Date: | Name: | Trainer Signature: |

Source: UI Healthcare Engineering Services

Date effective: October 12, 2016

Date Reviewed: