| SUBJECT/TITLE: | Operating a Gas Powered Tiller |
| --- | --- |
| PURPOSE: | Safe Operation of Gas Powered Tiller. |

Policy Statement:

The Engineering Services Department will provide proper training to staff that operate any Gas Powered Tiller.

Required PPE:

- Safety Glasses				4.   Hearing Protection, Ear Plugs, or Muffs

- Safety Shoes/ Boots with Reinforced Toe	5.   Appropriate gloves as needed

- Long Pants 					6.   High Visibility Vest as needed

Required Training:

- Read, understand, and follow manufacturer’s safety instructions.

- Training with qualified person prior to use.

| TASK | HAZARDS | CONTROLS |
| --- | --- | --- |
| Preparing Job Site And Equipment | Trips | Clear area within work zone; Remove trip hazards and/ or mark clearly hazards with cones, remove large branches, etc. |
|  | Cuts | Wear gloves when checking or clearing tines. |
|  | Exposure to Oil/Coolant | Wear safety glasses and gloves if adding any fluids. |
|  | Bodily Injury to Others | Identify work zone if needed use cones, barricades and other means necessary to keep pedestrian and other traffic out of the work zone if needed. |
| Operational Considerations | Bodily Injury | Wear reflective safety vest when working near roadways. |
|  |  | A pre-job discussion should occur to ensure both the equipment operator and assisting workers understand the scope of the project when needed. |
|  |  | Operator should keep watch for ground workers near equipment and ensure they are aware of operator's intended direction of movement. Use spotter as need to warn/watch for ground workers. |
|  |  | Ground workers should watch operator and equipment, staying clear of equipment's tines and flying debris. |
|  |  | All workers need to be aware of changing conditions at work site area. |
| Equipment Operations | Controlling Equipment | Ensure firm handle on both grips while engaged. Handle bars may tend to lift during clutch engagement. |
| Equipment Operations | Safety tips | Do not operate with one hand. |
|  |  | Do not operate until area dangers have been identified/ marked. |
|  |  | Operate within manufactures limitations. Be sure the drag bar is in place and properly adjusted. |
|  | Bodily Injury to Operator | Never reach into areas with moving parts such as tines. |
|  |  | Never leave equipment running to clear debris from tines or troubleshoot problems. |
|  |  | Do not operate damaged or malfunctioning equipment. |
|  |  | Be aware of changing conditions at worksite. |
|  |  | Be aware of fluid leaks. |
| After operations or during periods when area is not occupied by workers | Bodily Injury to Workers and Others | Operator should always leave equipment off. |
|  |  | Operator should ensure equipment is secured or staged so that it cannot be used by unauthorized personnel. |
|  |  | Workers should secure job site if needed with barricades, cones and signs to warn others to keep out of work site area. |
|  |  | Supervisor may place employee to watch job site if extreme hazards exist. |
| Servicing or Repair of Equipment | Bodily Injury | Obtain tag from shop, mark equipment "Do Not Use"- Specify problem. |
|  |  | Notify shop and/or take equipment to shop. |

Training: Operating a Gas Powered Tiller

Training Video: https://www.youtube.com/watch?v=PkRdVYvacnE

https://www.youtube.com/watch?v=Xmj8zYk0sQ0

DO NOT use this machine unless you have been trained in its safe use and operation. Training must be documented and signed by the employee before use.

| Description of Work: | Operating A Gas Powered Tiller |
| --- | --- |
|  | Potential Hazards: Exposed moving parts with the potential to cause harm through pinching, cutting, impact and crushing, ergonomics, vibration, noise, slips, trips and falls and dust. |
| Personal Protective Equipment (PPE) Required |
| Gloves | Face Masks | Eye Protection | Welding Mask | Appropriate Footwear | Hearing Protection | Protective Clothing |
| Safe Work Procedure Checklist |
| 1. PRE-Operation: Check for obvious faults and defects including fuel leaks or damage. Identify ON/OFF key switch. Wear adequate and appropriate PPE. 2. Operation: Always be looking ahead for obstacles. Watch for trees, buildings and other obstructions. Allow enough room to safely pass between obstructions. Be careful not to get too close. Keep hands firmly on handlebars. Ensure firm footing. Always keep eyes on direction of travel. Do not pull debris in tines when engine is running. Do not allow people to approach when tines are engaged. Know the limits of the machine. Use smooth operation on controls. Allow depth bar to drag and to its intended job. 3. POST-Operation: Ensure no damage has been made to unit or fluid leaks. Ensure tiller tines are free from debris and cleaned. Ensure equipment is returned to storage after use and full of fuel. |
| Competent Persons (The following persons are authorised to operate equipment.) |
| Date: | Name: | Trainer Signature: |

Source: UI Healthcare Engineering Services

Date effective: December 7, 2016

Date Reviewed: